| INTENDED USE Cable median barriers are commonly used in wider medians, where there is adequate room behind the barrier to allow a dynamic deflection of up to 138 inches [3500 mm]. The maximum run length for the system is 2000 feet [610 m]. This system must be anchored using a cable anchor and terminal system like SEC01. SGM-01a is a Test Level 3 barrier. COMPONENTS Unit length = 192 inches [4880 mm] Designator Component Number FBH01 Hook bolts and nuts 3 or FBH04 Hook bolts and nuts 3 PSE02 Post 1 RCM01 Cable (984 ft [300 m] typical) 3 APPROVALS FHWA Acceptance Letter B-64. REFERENCES R.B. Albin, D.L. Bullard, Jr., and W.L. Menges, “Washington State Cable Median Barrier,” Transportation Research Record 1743, Transportation Research Board, 2001. CONTACT INFORMATION Federal Highway Administration Office of Safety 400 Seventh Street, SW Washington, DC 20590 202-366-2288 |
| --- |
| WEAK-STEEL POST CABLE MEDIAN BARRIER |
| SGM01a |  |
| SHEET NO. | DATE |  |
| 2 of 2 | 8/10/05 |  |