| INTENDED USE Strong-post W-beam median barriers should be used in locations where a maximum dynamic deflection of 24 inches [600 mm] or less is acceptable. W-beam barriers should be anchored and terminated using a suitable end treatment. Both SGM-04a (steel posts) and SGM-04b (timber posts) with wood or approved plastic blockouts are Test Level 3 barriers. COMPONENTS Unit length = 150 inches [3810 mm] Designator Component System Number FBB01 Splice bolt and nut a-b 16 FBB03 Guardrail-post bolt and nut a 4 FBB05 Guardrail-post bolt and nut b 2 FWC16a Round washer a,b 4,2 PDB01a Timber post blockout b 4 PDB01b Timber post blockout a 4 PDE02 Timber post b 2 or PDE14 Round timber post b 2 PWE01 Steel post a 2 RWM02a W-beam rail a-b 2 APPROVALS FHWA Acceptance Letter B-64, 2/14/00. REFERENCES J.D. Michie and M.E. Bronstad, Location, Selection and Maintenance of Highway Traffic Barriers, National Cooperative Highway Research Program Report 118, Highway Research Board, 1971. M.D. Graham, W.C. Burnett, J.L. Gibson, and R.H. Freer, New Highway Barriers: The Practical Application of Theoretical Design, Highway Research Record 174, Highway Research Board, 1967. CONTACT INFORMATION Federal Highway Administration Office of Safety 400 Seventh Street, SW Washington, DC 20590 202-366-2288 |
| --- |
| STRONG-POST W-BEAM MEDIAN BARRIER |
| SGM04a-b |  |
| SHEET NO. | DATE |  |
| 2 of 2 | 07/06/2005 |  |