| INTENDED USE Strong-post W-beam median barriers should be used in locations where a maximum dynamic deflection of 24 inches [600 mm] or less is acceptable. W-beam barriers should be anchored and terminated using a suitable end treatment. Both SGM-06a (steel posts) and SGM-06b (timber posts) with wood or approved plastic blockouts are Test Level 3 barriers. COMPONENTS Unit length = 150 inches [3810 mm] Designator Component System Number FBB01 Splice bolt and nut a-b 16 FBB03 Guardrail-post bolt and nut a 4 FBB03 Bolt trimmed to 4 in [100 mm] a 4 FBB04 Bolt trimmed to 15 in [380 mm] b 2 FBB05 Guardrail-post bolt and nut b 2 FBX16a Rub rail splice bolts (1.5 in [40 mm]) and nuts a-b 8 PDB01a Timber post blockout b 4 PDB01b Timber post blockout a 4 PDE15 Timber post b 2 PWE05 Steel post a 2 RER01 Bent-plate rub rail a-b 2 or RLR01 Channel rub rail a-b 2 RWM02a W-beam rail a-b 2 APPROVALS FHWA Acceptance Letter B-64. REFERENCES M.E. Bronstad, J.D. Michie, and J.D. Mayer, Jr., Performance of Longitudinal Traffic Barriers, National Cooperative Highway Research Program Report 289, Transportation Research Board, 1987. J.D. Michie and M.E. Bronstad, Location, Selection and Maintenance of Highway Traffic Barriers, National Cooperative Highway Research Program Report 118, Highway Research Board, 1971. R.N. Field and R.H. Prysok, Dynamic Full-Scale Impact Tests of Double-Block-out Metal Beam Carriers and Metal Beam Guard Railing, California Division of Highway, 1965. CONTACT INFORMATION Federal Highway Administration Office of Safety 400 Seventh Street, SW Washington, DC 20590 202-366-2288 |
| --- |
| STRONG-POST MEDIAN BARRIER WITH RUB RAIL |
| SGM06a-b |  |
| SHEET NO. | DATE |  |
| 2 of 2 | 07/25/2005 |  |