| INTENDED USE Strong-post thrie-beam median barriers should be used in locations where a maximum dynamic deflection of 20 inches [500 mm] is acceptable. Thrie-beam barriers can be more effective than W-beam barriers in collisions with larger vehicles. This barrier system must be properly anchored and terminated. Any common W-beam terminal can be used in conjunction with an STG01 W-beam-to-thrie-beam transition to provide a crashworthy terminal and anchorage. SGM-09a (steel posts) and SGM09c (wood posts) with either PDB02a-b wood blockouts or approved composite blockouts are Test Level 3 barriers. SGM-09b (modified thrie-beam) is a Test Level 4 barrier. COMPONENTS Unit length = 150 inches [3810 mm] Designator Component System Number FBB01 Splice bolt and nut a,b,c 24,16,24 FBB02 Rail-blockout bolt and nut b 4 FBB03 Rail-blockout bolt and nut a 8 FBB05 Rail-blockout bolt and nut c 4 FBX16a Post-blockout bolt (1.5 inches [40 mm]) and nut b 8 FWC16a Round washer a,c 8,4 PDB02a Timber post blockout c 4 PDB02b Timber post blockout a 4 PDE03 Timber guardrail post c 2 PWB03 Modified thrie blockout b 4 PWE03 Steel guardrail post a 2 PWE04 Steel guardrail post b 2 RTB01a Thrie-beam backup plate b 2 RTM02a Thrie-beam rail a-c 2 APPROVALS FHWA Acceptance Letter B-64, 2/14/00. REFERENCES D.L. Ivey, R.R. Robertson and C.E. Buth, Test and Evaluation of W-Beam and Thrie-Beam Guardrails, Federal Highway Administration, FHWA-RD-82-071, Washington, D.C., 1986. C.E. Buth, W.L. Campise, L.I. Griffin, M.L. Love, and D.L. Sicking, Performance Limits of Longitudinal Barriers, Federal Highway Administration, Report No. FHWA-RD-86-153 (vol. 1), Washington, D.C., May 1986. M.E. Bronstad, J.D. Michie, J.D. Viner, and W.E. Behm, Crash Test Evaluation of the Thrie Beam Traffic Barrier, Highway Research Record, Highway Research Board, 1974. |
| --- |
| STRONG-POST THRIE-BEAM MEDIAN BARRIER |
| SGM09a-c |  |
| SHEET NO. | DATE |  |
| 2 of 4 | 7/06/2005 |  |

| CONTACT INFORMATION Federal Highway Administration Office of Safety 400 Seventh Street, SW Washington, DC 20590 202-366-2288 |
| --- |
| STRONG-POST THRIE-BEAM MEDIAN BARRIER |
| SGM09a-c |  |
| SHEET NO. | DATE |  |
| 4 of 4 | 7/06/2005 |  |