| INTENDED USE Cable guardrails are commonly used where there is adequate room behind the barrier to allow a dynamic deflection of up to 138 inches [3500 mm]. This system must be anchored using a cable anchor and terminal system like SEC01. SGR-01a and SGR-01b are both test level 3 barriers. COMPONENTS Unit length = 192 inches [5000 mm] Designator Component System Number FBH01 Hook bolts and nuts a-b 3 or FBH04 Hook bolts and nuts a-b 3 or FBH03 Hook bolts and nuts a 3 PFE01 Post b 1 with PLS02 Soil plate b 1 and FBX08a Bolt (2.5 in [65 mm]) and nut b 2 PSE01 Post a 1 RCM01 Cable (984 ft [300 m] typical) a-b 3 APPROVALS FHWA Acceptance Letter B-64, 2/14/00. REFERENCES M.D. Graham, W.C. Burnett, J.L. Gibson, R.H. Freer, New Highway Barriers: The Practical Application of Theoretical Design, Highway Research Record 174, Highway Research Board, Washington, DC, 1967, pp. 88-183. M.E. Bronstad, J.E. Michie and J.D. Mayer, Jr., Performance of Longitudinal Traffic Barriers, National Cooperative Highway Research Program Report Number 289, Transportation Research Board, June, 1987. J.B. Mayer, Jr., Crash-Test Evaluation of a Franklin Post and Cable Guardrail System, Southwest Research Institute Test Reports prepared for the South Dakota Department of Transportation, Pierre, SD, August, 1989. CONTACT INFORMATION Federal Highway Administration Office of Safety 400 Seventh Street, SW Washington, DC 20590 202-366-2288 |
| --- |
| WEAK-STEEL POST CABLE GUARDRAIL |
| SGR01a-b |  |
| SHEET NO. | DATE |  |
| 2 of 2 | 07/12/2005 |  |