| INTENDED USE Weak-post W-beam guardrails are commonly used where dynamic deflections of at least 87 inches [2200 mm] are acceptable. This system must be anchored with a suitable terminal system; crashworthy W-beam terminals can be transitioned to and used with this guardrail system. SGR-02a is a Test Level 2 barrier. COMPONENTS Unit length = 150 inches [3810 mm] Designator Component Number FBB01 Splice bolts and nuts 8 FBX08a Rail-post bolt (1.5 [40]) and nut 1 FBX14a Rail support bolt (1.5 [40]) and nut 1 FWR01 Guardrail washer 1 PSE03 Post 1 RWM02a W-beam rail 1 APPROVALS FHWA Acceptance Letter B-64. REFERENCES M.E. Bronstad, J.E. Michie and J.D. Mayer, Jr., Performance of Longitudinal Traffic Barriers, National Cooperative Highway Research Program Report Number 289, Transportation Research Board, June, 1987. J.D. Michie, L.R. Calcote, and M.E. Bronstad, Guardrail Performance and Design, National Cooperative Highway Research Program Report Number 115, Highway Research Board, 1971. CONTACT INFORMATION Federal Highway Administration Office of Safety 400 Seventh Street, SW Washington, DC 20590 202-366-2288 |
| --- |
| WEAK-POST W-BEAM GUARDRAIL |
| SGR02a |  |
| SHEET NO. | DATE |  |
| 2 of 2 | 07/20/2005 |  |