| INTENDED USE Weak-post box-beam guardrails are commonly used where dynamic deflections of at least 59 inches [1500 mm] are acceptable. This system must be anchored with a suitable terminal system. SGR-03 is a Test Level 3 barrier. COMPONENTS Unit length = 216 inches [5490 mm] Designator Component Number FBX08a Hex-bolt (7-7/8 [200]) and nut 3 FBX12a Hex-bolt (2 [50]) and nut 3 FBX20b Hex-bolt (2 [50]) and nut 8 FPP01 Shelf bracket 3 FWC08a Washer 6 FWC12a Washer 3 FWC20b Washer 8 PSE08 Post and soil plate 3 RBM01 Box-beam rail 1 RBS01 Splice plate 2 APPROVALS FHWA Acceptance Letter B-64. REFERENCES K.K. Mak, R.P. Bligh, and W.L. Menges, Testing of State Roadside Safety Systems, Volume XI, Appendix J: Crash Testing and Evaluation of Existing Guardrail Systems, Report No. FHWA-RD-98-046, Federal Highway Administration, 1990. M.E. Bronstad, J.E. Michie, and J.D. Mayer, Jr., Performance of Longitudinal Traffic Barriers, National Cooperative Highway Research Program Report Number 289, Transportation Research Board, 1987. J.D. Michie and M.E. Bronstad, Location, Selection, and Maintenance of Highway Traffic Barriers, National Cooperative Highway Research Program Report Number 118, Highway Research Board, 1971. CONTACT INFORMATION Federal Highway Administration Office of Safety 400 Seventh Street, SW Washington, DC 20590 202-366-2288 |
| --- |
| WEAK-POST BOX-BEAM GUARDRAIL |
| SGR03 |  |
| SHEET NO. | DATE |  |
| 2 of 2 | 8/10/05 |  |