| INTENDED USE Strong-post W-beam guardrails should be used in locations where a maximum dynamic deflection of 36 inches [900 mm] or less is acceptable. W-beam guardrails should be anchored and terminated using a suitable end treatment. SGR-04a (steel posts) with steel blockouts is a Test Level 2 barrier. SGR-04b (wood posts) with wood, steel or plastic blockouts is a Test Level 3 barrier; SGR-04c (steel posts) with wood or plastic blockouts is also a Test Level 3 barrier. COMPONENTS Unit length = 150 inches [3810 mm] Designator Component System Number FBB01 Splice bolt and nut a-c 8 FBB02 Guardrail-post bolt and nut a 2 FBB03 Guardrail-post bolt and nut c 2 FBB04 Guardrail-post bolt and nut b 2 FBX16a Post blockout bolt (1.5 inches [40 mm]) and nut a 4 FWC16a Round washer b,c 2 PDB01a Timber post blockout b 2 PDB01b Timber post blockout c 2 PDE02 Timber post b 2 or PDE13 Timber post b 2 PWB01 Steel post blockout a 2 PWE01 Steel post a,b 2 or PWE02 Steel post a,b 2 RWB01a W-beam backup plate a 1 RWM02a W-beam rail a-c 1 APPROVALS FHWA Acceptance Letter B-64, 2/14/00. REFERENCES M.E. Bronstad, J.E. Michie and J.D. Mayer, Jr., Performance of Longitudinal Traffic Barriers, National Cooperative Highway Research Program Report Number 289, Transportation Research Board, June, 1987. C.E. Buth, W.L. Campise, L.I. Griffin, M.L. Love, and D.L. Sicking, Performance Limits of Longitudinal Barriers, Federal Highway Administration, Report No. FHWA-RD-86-153 (vol. 1), Washington, D.C., May 1986. R.L. Stoughton, R.L. Stoker, E.F. Nordlin, Dynamic Tests of Metal Beam Guardrail, Transportation Research Record, Transportation Research Board, Washington, D.C., 1975. |
| --- |
| STRONG-POST W-BEAM GUARDRAIL |
| SGR04a-c |  |
| SHEET NO. | DATE |  |
| 2 of 4 | 6/30/05 |  |

| CONTACT INFORMATION Federal Highway Administration Office of Safety 400 Seventh Street, SW Washington, DC 20590 202-366-2288 |
| --- |
| STRONG-POST W-BEAM GUARDRAIL |
| SGR04a-c |  |
| SHEET NO. | DATE |  |
| 4 of 4 | 6/15/05 |  |