| INTENDED USE The culvert-mounted W-beam guardrail is often used to cross box culverts or other small structures that interrupt a length of soil-mounted SGR04 guardrail. This is a Test Level 3 barrier. COMPONENTS Unit length = 150 inches [3810 mm] Designator Component Number FBB01 Splice bolt and nut 8 FBB03 Post-blockout bolt and nut 2 FBX20a Anchor bolt (7 inches [175 mm]) and nut 8 or FRS20a Anchor stud and nut 8 FPB03 Bearing plate 2 FWC16a Round washer 2 FWC20a Anchor bolt washer 16 PDB01b Steel guardrail blockout 2 PWF01 Deck-mounted steel guardrail post 2 RWB01a W-beam backup plate 1 RWM02a W-beam rail 1 APPROVALS This system is a variation of SGR04, which is included in FHWA Acceptance Letter B-64. REFERENCES T.J. Hirsch and D. Beggs, “Use of Guardrails on low-fill bridge-length culverts,” in Roadside Safety Features, Transportation Research Record 1198, National Research Council, Washington, DC, 1980. CONTACT INFORMATION Federal Highway Administration Office of Safety 400 Seventh Street, SW Washington, DC 20590 202-366-2288 |
| --- |
| CULVERT-MOUNTED W-BEAM GUARDRAIL |
| SGR05 |  |
| SHEET NO. | DATE |  |
| 2 of 2 | 8/04/05 |  |