| INTENDED USE Strong-post thrie-beam guardrails should be used in locations where there is at least 24 in. [600 mm] of available deflection space. Any common W-beam terminal can be used in conjunction with an STG01 W-beam-to-thrie-beam transition to provide a crashworthy terminal and anchorage. SGR-09a (steel posts) and SGR09c (wood posts) with either PDB02a-b wood blockouts or approved composite blockouts are Test Level 3 barriers. SGR-09b (modified thrie-beam) is a Test Level 4 barrier. COMPONENTS Unit length = 150 in. [3810 mm] Designator Component System Number FBB01 Splice bolt and nut a,b,c 12,8,12 FBB02 Rail-blockout bolt and nut b 2 FBB03 Rail-blockout bolt and nut a 4 FBB04 Rail-blockout bolt and nut c 4 FBX16a Post-blockout bolt (1.5 inches [40 mm]) and nut b 4 FWC16a Round washer a,c 4 PDB02a Timber post blockout c 2 PDB02b Timber post blockout a 2 PDE01 Timber guardrail post c 2 PWB03 Modified thrie blockout b 2 PWE03 Steel guardrail post a 2 PWE04 Steel guardrail post b 2 RTM02a Thrie-beam rail a-c 1 RTB01a Thrie-beam backup plate a-b 1 APPROVALS FHWA Acceptance Letter B-64, 2/14/00. REFERENCES M.E. Bronstad, J.E. Michie and J.D. Mayer, Jr., Performance of Longitudinal Traffic Barriers, National Cooperative Highway Research Program Report Number 289, Transportation Research Board, June, 1987. D.L. Ivey, R.R. Robertson and C.E. Buth, Test and Evaluation of W-Beam and Thrie-Beam Guardrails, Federal Highway Administration, FHWA-RD-82-071, Washington, D.C., 1986. C.E. Buth, W.L. Campise, L.I. Griffin, M.L. Love, and D.L. Sicking, Performance Limits of Longitudinal Barriers, Federal Highway Administration, Report No. FHWA-RD-86-153 (vol. 1), Washington, D.C., May 1986. |
| --- |
| STRONG-POST THRIE-BEAM GUARDRAIL |
| SGR09a-c |  |
| SHEET NO. | DATE |  |
| 2 of 3 | 07/06/2005 |  |

| CONTACT INFORMATION Federal Highway Administration Office of Safety 400 Seventh Street, SW Washington, DC 20590 202-366-2288 |
| --- |
| STRONG-POST THRIE-BEAM GUARDRAIL |
| SGR09a-c |  |
| SHEET NO. | DATE |  |
| 3 of 3 | 07/06/2005 |  |