| INTENDED USE SGR40 is an NCHRP Report 350 TL-2 T-intersection system. Layout of this system is shown on Sheet 1 of 2, and described below. The T-intersection system is a 27 in. [690 mm] high rail system. The nose section of this T-intersection system consists of a 12.5 ft. [3.82 m] curved W-beam segment which has an 8 ft. [2.44 m] radius. The curved section is attached to a straight W-beam section on the secondary road via common W-beam splicing details. The secondary road W-Beam should have a 25 ft. [7.62 m] minimum length and should be terminated with a positive anchor. Five Controlled Released Terminal (CRT) posts, spaced at 6.25 ft. [1.91 m], are placed along the curved section and secondary road section. On the primary road direction, the curved section is spliced to a 6.25 ft. [1.91 m] short W-beam segment at CRT post 7. The short W-beam section has also two 7-7/8 × 7-7/8 × 72 in. [200 × 200 × 1980 mm] posts embedded 44 in. [1117.6 mm] in soil. Starting at post 8, a stiffer rail section is used to act as a transition to the bridge rail. The transition section consists of the 6.25 ft. [1905 mm] short W-beam segment which is spliced to a 12.5 ft. [3810 mm] W-beam guardrail. The W-beam guardrail is backed by an MC 8 × 22.8 [MC 200 x 33.9] structural steel channel which runs from post 9 to the bridge barrier. The transition has three timber posts which are 9-7/8 × 9-7/8 × 78 inches [250 × 250 × 1980 mm]. They are embedded 50 in. [1270 mm] in soil (Post Detail A). The five timber posts (post 8 to post 12) have 7-7/8 × 7-7/8 × 14 in. [200 × 200 × 360 mm] wood blockouts. See FHWA Acceptance Letter B-209 for additional information and acceptable modifications. Details of the system are available upon request. APPROVALS Federal Highway Administration (FHWA) Eligibility Letter B-209, November 10, 2010. CONTACT INFORMATION Texas A&M Transportation Institute Texas A&M University System 3135 TAMU College Station, Texas 77843-3135 (979) 845-1713 http://tti.tamu.edu |
| --- |
| TL-2 T-INTERSECTION SHORT RADIUS GUARDRAIL SYSTEM |
| SGR40 |  |
| SHEET NO. | DATE |  |
| 2 of 2 | 10/31/2013 |  |